PMO NEGROS ORIENTAL/SIQUIJOR

BIDS AND AWARDS COMMITTEE-PGS

13 September 2017

SUPPLEMENTAL/BID BULLETIN NO.  1

AMENDMENTS TO THE BID DOCUMENTS  FOR THE PROCUREMENT OF THE :

SUPPLY, DELIVERY AND INSTALLATION INCLUDING TESTING AND COMMISSIONING OF THE FOLLOWING:

- TWO (2) UNITS 150KVA GENERATOR SETS WITH AUTOMATIC TRANSFER SWITCH AT THE PORT OF DUMAGUETE, AND

- ONE (1) UNIT 100KVA GENERATOR SET WITH AUTOMATIC TRANSFER SWITCH AT THE PORT OF SIQUIJOR.

This Supplemental/Bid Bulletin is issued to amend the Bid Documents of the above-named project.

The amendments are as follows:

| ORIGINAL (OLD) | AMENDMENT (NEW) |
| --- | --- |
| Item No. 3 of Section VI. Schedule of Requirements. “3)Other Requirements Professional Electrical Engineer Civil Engineer | Item No. 3 of Section VI. Schedule of Requirements. “3)Other Requirements Professional Electrical Engineer Civil Engineer Fuel tank of all genset units shall be full upon turn-over to the Authority. Provision of Three (3) Units manually operated mechanical pump. NOTE : Attached hereto is the amended Section VI. Schedule of Requirements and Bid Form T.2 Schedule of Requirements which will be submitted to the Authority as part of the bidder’s First Envelope. |
| ORIGINAL ( OLD ) | AMENDMENT (NEW) |
| Item No .2 (8) Scope of Work of the Terms of Reference “8. Shall include the processing and securing of Permit to Operate for the three (3) units of Generator set at the Ports of Dumaguete and Siquijor. “ Item No. 6 Other Conditions of the Terms of Reference “ 4. Contractor/Supplier must have a service center within Dumaguete City with 24/7 on-call service.” | Item No .2 (8) Scope of Work of the Terms of Reference Item No .2 (8) Terms of Reference, Scope of Work: “8. Shall include the processing and securing of Permit to Operate for the three (3) Generator set in the Ports of Dumaguete and Siquijor. Further, the winning bidder is responsible to secure all permits and license as required by law and government agencies concerned including the processing and payments which are necessary to the accomplishment of the Scope of Work. Item No. 6 Terms of Reference and other Conditions. “ 4. Contractor/Supplier must have a service center within Dumaguete City and/or assigned technician based in Dumaguete who will perform monthly monitoring check-up for the generator sets and 24/7 on call service. Moreover, assigned technician should be a regular employee of the winning bidder” |
|  | Item No. 2. (4) Scope of Work of the Terms of Reference Attached hereto is the amended Engineering Plans and Drawings for the Provision of Power House at the Port of Dumaguete |

For information and guidance of all concerned.

(SGD.)JENLYN MEDIANA B. ARENASA

Chairperson, BAC-PGS

Section VI. Schedule of Requirements

| Item | Specifications | No. of Units | Location | Delivery Schedule |
| --- | --- | --- | --- | --- |
| 1)Genset, 150KVA | A. Engine Specification |  | 2 | Port of Dumaguete | 60 CD |
|  | Configuration | In-line, 6 Cylinders |  |  |  |
|  | Aspiration | Turbocharged after water-cooling |  |  |  |
|  | Starting Voltage | 24V |  |  |  |
|  | Prime Rating Power | 108kW/135kVA |  |  |  |
|  | Standby Rating Power | 120kW/150KVA |  |  |  |
|  | Rated Speed RPM | 1800 |  |  |  |
|  | Control Panel | Digital |  |  |  |
|  | Governor Type | Electrical |  |  |  |
|  | Cooling System | Water Cooling Cycle |  |  |  |
|  | Phase | 3 |  |  |  |
|  | Insulation | Class H |  |  |  |
|  | Fuel Consumption @ 100% Load (L/Hr.) | 24 |  |  |  |
|  | Frequency | 60 Hz |  |  |  |
|  | Power Factor | 0.8 |  |  |  |
|  | Volt | 230Vac |  |  |  |
|  | Exciter Type | Single bearing, Brushless, Self-excited |  |  |  |
|  | B. Body/Enclosure | Soundproof/weather proof |  |  |  |
|  | C. Provision of Powerhouse | According to attached engineering plans and drawings |  |  |  |
| 2)Genset, 100KVA | A. Engine Specification |  | 1 | Port of Siquijor | 60 CD |
|  | Configuration | In-line, 6 Cylinders |  |  |  |
|  | Aspiration | Turbocharged after water-cooling |  |  |  |
|  | Starting Voltage | 24V |  |  |  |
|  | Prime Rating Power | 72kW/90kVA |  |  |  |
|  | Standby Rating Power | 80kW/100KVA |  |  |  |
|  | Rated Speed RPM | 1800 |  |  |  |
|  | Control Panel | Digital |  |  |  |
|  | Governor Type | Electrical |  |  |  |
|  | Cooling System | Water Cooling Cycle |  |  |  |
|  | Phase | 3 |  |  |  |
|  | Insulation | Class H |  |  |  |
|  | Fuel Consumption @ 100% Load (L/Hr.) | 24 |  |  |  |
|  | Frequency | 60 Hz |  |  |  |
|  | Power Factor | 0.8 |  |  |  |
|  | Volt | 230Vac |  |  |  |
|  | Exciter Type | Single bearing, Brushless, Self-excited |  |  |  |
|  | B. Body/Enclosure | Soundproof/ weather proofed |  |  |  |
|  | C. Provision of Powerhouse | According to attached engineering plans and drawings |  |  |  |
| 3)Other Requirements | 1. Professional Electrical Engineer | Five (5) years minimum employment in the company |  |  |  |
|  | 2. Civil Engineer | Five (5) years minimum employment in the company |  |  |  |
|  | 3. Fuel tank of all genset units shall be full upon turn-over to the Authority |  |  |  |  |
|  | 4..Provision of Three (3) Units manually operated mechanical fuel pump. |  |  |  |  |

The schedule stipulates the number of Generator Sets and Powerhouses and their location.

| T.2 Sections VI. Schedule of Requirements The delivery schedule expressed as days/weeks/months stipulates hereafter a delivery date which is the date of delivery to the project site. |  |
| --- | --- |
| Item | Specifications | No. of Units | Location | Delivery Schedule |
| 1)Genset, 150KVA | A. Engine Specification |  | 2 | Port of Dumaguete | 60 CD |
|  | Configuration | In-line, 6 Cylinders |  |  |  |
|  | Aspiration | Turbocharged after water-cooling |  |  |  |
|  | Starting Voltage | 24V |  |  |  |
|  | Prime Rating Power | 108kW/135kVA |  |  |  |
|  | Standby Rating Power | 120kW/150KVA |  |  |  |
|  | Rated Speed RPM | 1800 |  |  |  |
|  | Control Panel | Digital |  |  |  |
|  | Governor Type | Electrical |  |  |  |
|  | Cooling System | Water Cooling Cycle |  |  |  |
|  | Phase | 3 |  |  |  |
|  | Insulation | Class H |  |  |  |
|  | Fuel Consumption @ 100% Load (L/Hr.) | 24 |  |  |  |
|  | Frequency | 60 Hz |  |  |  |
|  | Power Factor | 0.8 |  |  |  |
|  | Volt | 230Vac |  |  |  |
|  | Exciter Type | Single bearing, Brushless, Self-excited |  |  |  |
|  | B. Body/Enclosure | Soundproof/weather proof |  |  |  |
|  | C. Provision of Powerhouse | According to attached engineering plans and drawings |  |  |  |
| 2)Genset, 100KVA | A. Engine Specification |  | 1 | Port of Siquijor | 60 CD |
|  | Configuration | In-line, 6 Cylinders |  |  |  |
|  | Aspiration | Turbocharged after water-cooling |  |  |  |
|  | Starting Voltage | 24V |  |  |  |
|  | Prime Rating Power | 72kW/90kVA |  |  |  |
|  | Standby Rating Power | 80kW/100KVA |  |  |  |
|  | Rated Speed RPM | 1800 |  |  |  |
|  | Control Panel | Digital |  |  |  |
|  | Governor Type | Electrical |  |  |  |
|  | Cooling System | Water Cooling Cycle |  |  |  |
|  | Phase | 3 |  |  |  |
|  | Insulation | Class H |  |  |  |
|  | Fuel Consumption @ 100% Load (L/Hr.) | 24 |  |  |  |
|  | Frequency | 60 Hz |  |  |  |
|  | Power Factor | 0.8 |  |  |  |
|  | Volt | 230Vac |  |  |  |
|  | Exciter Type | Single bearing, Brushless, Self-excited |  |  |  |
|  | B. Body/Enclosure | Soundproof/ weather proofed |  |  |  |
|  | C. Provision of Powerhouse | According to attached engineering plans and drawings |  |  |  |
| 3)Other Requirements | 1. Professional Electrical Engineer | Five (5) years minimum employment in the company |  |  |  |
|  | 2. Civil Engineer | Five (5) years minimum employment in the company |  |  |  |
|  | 3. Fuel tank of all genset units shall be full upon turn-over to the Authority |  |  |  |  |
|  | 4..Provision of Three (3) Units manually operated mechanical fuel pump. |  |  |  |  |

# Text boxes

Submitted by:

Bidder’s Representative/Authorized Signatory                                        Date: